MSM-101

MICROPROCESSORIZED FLUXMETER

The Fluxmeter MSM-101 is microprocessorized equipment designed to measure the quasistatic changes of magnetic flux association with induction sensors commonly used in measurements of hard and soft magnetic materials properties

# EQUIPMENT

The MSM-101 meter contains:

- Cover,

- Supply unit,

- DTR – 2 pieces.

# TECHNICAL DATA

Conversion:						analogue,

Measurement range:					(0.1,   0.01,    0.001) Wb/V,

Resolution:						(1·10-1,	1·10-2, 1·10-3) mWb/V

Drift	(7·10-6 Wb/min, (after Fluxmeter thermal stabilization and precise the offset adjustment),

Input resistance:					10k,

Accuracy of integration:				0.3%,

The fluxmeter constant don't changes for: 		R < 500

Supply:						230V, 50Hz

Supply							accumulator

Signalling of necessity of charging a battery		acoustic and graphic

Operating conditions:

- ambient temperature				0(C ( + 50(C

- air relative humidity				20 % ( 80 %

# DIMENSION

all dimensions in mm